## Slide 1
王昊翔
WANG Haoxiang
hxwang@scut.edu.cn
School of Computer Science & Engineering
COMPUTER NETWORKS

## Slide 2
Chapter 2. The Physical Layer
Part 1

## Slide 3: Contents
Theoretical basis for data communication
  Fourier analysis
  Bandwidth-Limited Signals
  The Maximum data rate of a channel
Guided transmission media
  Magnetic media
  Twisted pair
  Coaxial cable
Wireless Transmission
  Electromagnetic spectrum
  Radio transmission
  Microwave transmission
  Infrared and millimeter waves
  Light wave transmission

## Slide 4: The physical layer
defines the mechanical, electrical, and timing interfaces to the network, provides the means to transmit bits from sender to receiver, that is, involves a lot on how to use (analog) signals for digital information.

## Slide 5: Theoretical Basis
Information can be transmitted on wires by varying some physical property such as voltage or current. By representing the value of this voltage or current as a single-valued function of time, f(t), we can model the behavior of the signal and analyze it mathematically. This analysis is the subject of the following sections.

## Slide 6: Fourier Series (Not required, but…)
Any reasonably behaved periodic function, g(t), with period T can be constructed by summing a (possibly infinite) number of sines and cosines:
where f=1/T is the fundamental frequency and an and bn are the sine and cosine amplitudes of the nth harmonics (terms).

## Slide 7: Fourier Series(Not required, but…)

## Slide 8: An example(Not required)
Consider 01100010, 8 bit for ASCII character 'b':
  an =1/πn[cos(πn/4) -cos(3πn/4) + cos(6πn/4) -cos(7πn/4)]
  bn = 1/πn[sin(3πn/4) -sin(πn/4) + sin(7πn/4) -sin(6πn/4)]
  cn = ¾
  The root mean square amplitudes is

## Slide 9
Note: root mean squares (on the right) reflect the dispersed
energy at the given frequency.

## Slide 10: Bandwidth
Digital signal transmission is subject to attenuation, distortion, etc. This is partly caused by disallowing high-frequency components to pass through.
The range of frequency or the number of bits of a transmission medium is called bandwidth.

## Slide 11: Bandwidth-Limited Signals
The larger n is, the higher the frequency nf of the nth harmonic.
All transmission facilities diminish different Fourier components by different amounts, thus introducing distortion.
Usually, the amplitudes are transmitted undiminished from 0 up to some frequency fc (in Hertz, Hz) with all frequencies above this cutoff frequency截止频率 strongly attenuated.

## Slide 12: Signal-to-Noise Ratio
S/N
  S: signal power
  N: noise power
dB
  10 log10 S/N
  an S/N ratio of 1000 is 30 dB

## Slide 13: Max. Data Rate of a Channel
Nyquist’s Theorem (noiseless channel)
  H: bandwidth
  V: discrete levels
  Maximum data rate: 2H log2 V bits/sec
Shannon’s Theorem (noise channel)
  H: bandwidth
  S/N: signal to noise ratio
  Maximum number of bits/sec: H log2 (1 + S/N)

## Slide 14: Exercise
Suppose that the bandwidth of a channel is between 3MHz and 4MHz and SN = 24dB.
  (1) what is the capacity of this channel?
  (2) Being able to achieve capacity, how many signaling levels are required?

## Slide 15: Exercise solution
Suppose that the bandwidth of a channel is between 3MHz and 4MHz and SN = 24dB.
  (1) what is the maximum data rate?
    H = 1MHz
    S/N = 251
    C = 106xlog2(1+251)=8Mbps
  (2) Being able to achieve capacity, how many signaling levels are required?
    C=2H log2 V
    V=16

## Slide 16: Guided Transmission Media
  Magnetic media
  Twisted pair
  Coaxial cable
  Fiber optics

## Slide 17
Various Types of Network Media

## Slide 18: Magnetic media
Never underestimate the bandwidth of a station wagon full of tapes hurtling down the highway
  Take a standard videotape that can carry about 200 gigabytes of data.
  A box of 60 x 60 x 60 cm can hold about 1000 tapes, which corresponds to 200TB, or 1600Tb.
  Sending such a box can be done within 24 hours, worldwide, 19Gbps; or 400Gbps within one hour.
  Costs: roughly $5000 to ship 200TB, 3 cents for 1GB
So, why not just tape?

## Slide 19: Twisted pair
UTP (Unshielded Twisted Pair)
STP (Shielded Twisted Pair)
10Base-T: 10Mbps, 100 meters
100Base-T: 100Mbps, 100 meters
1000Base-T: 1Gbps, 100 meters
Category 3: not to use anymore
Category 5/Super Category 5
Category 6/7: for Gigabit transmission

## Slide 20: Twisted pair (cont.)
棕
白棕
白兰
白橙
白绿
绿
兰
橙
8
7
6
5
4
3
2
1
8
7
6
5
4
3
2
1
Brown
White/Brown
Green
White/Blue
Blue
White/Green
Orange
White/Orange

## Slide 21: UTP in actions
Telephone line serve 3KM-5KM
  One pair only
Data Cable serve 100M, Four pairs
  Category 3 : 16MHz
  Category 5 : 100MHz
  Category 6 : 250MHz
  Category 7 : 600MHz
Data rate: 10Mbps, 100Mbps, 1000Mbps

## Slide 22
Coaxial cable consists of a hollow outer cylindrical conductor that surrounds a single inner wire made of two conducting elements.
It can be run, without as many boosts from repeaters, for longer distances between network nodes than either shielded or unshielded twisted-pair cable
Coaxial cable (50/75ohm:1GHz)

## Slide 24
advantages.
  It is easy to install
  is less expensive
  its real advantage is its size.
disadvantages
  is more prone to electrical noise and interference
  once considered slower at transmitting data than other types of cable.
  today, UTP is considered the fastest copper-based media.
  The distance between signal boosts is shorter for unshielded twisted-pair than it is for coaxial cable.
UTP vs. STP and COAX

## Slide 25: Fiber optics
Based on light refraction:
  Three examples of a light ray from inside a silica fiber impinging on the air/silica boundary at different angles.
  Light trapped by total internal reflection.

## Slide 26
  As it turns out, attenuation is extremely well in optical fiber. This means that they can be used for long distances. In addition, the bandwidth is enormous.
Item | LED | Semiconductor Laser
Data rate | Low | High
Mode | Multimode | Multimode or single mode
Distance | Short | Long
Lifetime | Long life | Short life
Temperature sensitivity | Minor | Substantial
Cost | Low cost | Expensive

## Slide 27
Fiber-optic cable is a networking medium capable of conducting modulated light transmissions. It is not susceptible to electromagnetic interference and is capable of higher data rates than any of the other types of networking media discussed here. Fiber-optic cable does not carry electrical impulses, signals that represent bits, are converted into beams of light. light in fibers is not considered wireless because the electromagnetic waves are guided in the optical fiber.
MM: multi-mode
SM: single-mode
LED-Light Emitting Diode
Semiconductor Laser
Fiber optics

## Slide 28: Fiber Connections
Observation: An interface consists of a receiver (photodiode) which transforms light into electrical signals, and/or a transmitter (LED or laser-diode)
Passive interface: A computer is directly connected to the optical fiber
Active interface: There’s an ordinary electrical repeater connected to two fiber segments and the computer:

## Slide 29
ST：插入锁定
光耦合器（ST）
SC：568A标准，方形，插入锁定

## Slide 30: Optical Fiber vs. Copper Wire (1)
Bandwidth: Fiber can support enormous bandwidths, exactly what we need with upcoming image-based applications (video-on-demand).
Attenuation: Because the attenuation in fiber is less than in copper (can you imagine why?), we don’t need to boost the signal as often. In practice, fiber requires an active repeater every 30 km, copper every 5 km.

## Slide 31: Optical Fiber vs. Copper Wire (2)
External influences: That’s right, no more interference from other cables, radios, power failures, etc.
Weight: Fiber simply doesn’t weigh as much. Good for backbones, and the use of heavy maintenance equipment.

## Slide 32: Wireless Transmission
The Electromagnetic Spectrum
Radio Transmission
Microwave Transmission
Infrared and Millimeter Waves
Lightwave Transmission

## Slide 33: The Electromagnetic Spectrum
f (Hz) 100 102 104 106 108 1010 1012 1014 1016 1018 1020 1022 1024
Visible
Light
Radio
Microwave
Infrared
UV
X-ray
Gamma Ray
f (Hz) 104 105 106 107 108 109 1010 1011 1012 1013 1014 1015 1016
Twisted Pair
Coax
Maritine
AM
Radio
FM
Radio
TV
Satellite
Terrestrial
Microwave
Fiber
Optics
HF
EHF
LF
MF
VHF
UHF
SHF
THF
Band
L: low
M: medium
H: high
V: very
U: ultra
S: super
E: extremely
T: tremendously

## Slide 34: Wave Properties
Radio, Microwaves, Infrared, and Visible Light
  can all be used for transmitting information
  AM, FM, or PM
UV, X-rays, and Gamma Rays
  would be even better due to their higher frequencies
  hard to produce and modulate
  do not propagate well through buildings
  dangerous to living things

## Slide 35: Radio Transmission
Radio waves
  easy to generate
  can travel long distances
  penetrate buildings easily
  omnidirectional
  at low frequencies, the power falls off sharply with distance from the source
  at high frequencies, radio waves tend to travel in straight lines and bounce off obstacles

## Slide 36: Propagation of Radio Waves
VLF, LF, and MF bands
Ionosphere
HF and VHF bands
Earth
Earth
Radio waves follow
the ground

## Slide 37: Microwave Transmission
Microwaves
  travel in straight lines
    can be narrowly focused (by a dish)
    the transmitting and receiving antennas must be accurately aligned with each other.
  do not pass through buildings well.
  can be absorbed by water/rain
  widely used for long-distance telephone communication, cellular telephones, TV distribution

## Slide 38: Infrared and Millimeter Waves
widely used for short-range communication.
  TV remote controller
do not pass through solid objects.
  Bad: limited distance
  Good: security
candidate for indoor wireless LAN
cannot be used outdoors (due to sun shines)

## Slide 39: Lightwave Transmission
Each side needs its own laser and its own photodetector.
The laser’s strength, a very narrow beam, is its weakness.
  Difficult aiming at far distance
offers high bandwidth
easy to install

## Slide 40: Summary
Data communication and computer networking have solid theorectical background.
Three major transmission media are widely used today: twisted pair, coaxial cable and optical fiber.
Wireless transmission becomes more and more important in today's networking.