## Slide 1
王昊翔
WANG Haoxiang
hxwang@scut.edu.cn
School of Computer Science & Engineering
国家双语教学试点项目 广东省精品课
COMPUTER NETWORKS 2023: Fall
- Chapter 2. The Physical Layer 1

## Slide 2: Contents
Theoretical basis for data communication
  Fourier analysis
  Bandwidth-Limited Signals
  The Maximum data rate of a channel
Guided transmission media
  Magnetic media
  Twisted pair
  Coaxial cable
Wireless Transmission
  Electromagnetic spectrum
  Radio transmission
  Microwave transmission
  Infrared and millimeter waves
  Light wave transmission

## Slide 3: The physical layer
defines the mechanical, electrical, and timing interfaces to the network, provides the means to transmit bits from sender to receiver, that is, involves a lot on how to use (analog) signals for digital information.

## Slide 4: Theoretical Basis
Information can be transmitted on wires by varying some physical property such as voltage or current. By representing the value of this voltage or current as a single-valued function of time, f(t), we can model the behavior of the signal and analyze it mathematically. This analysis is the subject of the following sections.

## Slide 5: Fourier Series
Any reasonably behaved periodic function, g(t), with period T can be constructed by summing a (possibly infinite) number of sines and cosines:
where f=1/T is the fundamental frequency and an and bn are the sine and cosine amplitudes of the nth harmonics (terms).

## Slide 6: Fourier Series

## Slide 7: An example
Consider 01100010, 8 bit for ASCII character 'b':
  an =1/πn[cos(πn/4) -cos(3πn/4) + cos(6πn/4) -cos(7πn/4)]
  bn = 1/πn[sin(3πn/4) -sin(πn/4) + sin(7πn/4) -sin(6πn/4)]
  cn = ¾
  The root mean square amplitudes is

## Slide 8
Note: root mean squares (on the right) reflect the dispersed
energy at the given frequency.

## Slide 9: Bandwidth
Digital signal transmission is subject to attenuation, distortion, etc. This is partly caused by disallowing high-frequency components to pass through.
The range of frequency or the number of bits of a transmission medium is called bandwidth.

## Slide 10: Bandwidth-Limited Signals
The larger n is, the higher the frequency nf of the nth harmonic.
All transmission facilities diminish different Fourier components by different amounts, thus introducing distortion.
Usually, the amplitudes are transmitted undiminished from 0 up to some frequency fc (in Hertz, Hz) with all frequencies above this cutoff frequency截止频率 strongly attenuated.

## Slide 11: Bandwidth
Hz
bps
？

## Slide 12: Bit Rate vs. Harmonics
Given a bit rate of b bits/sec, the time T required to send 8 bits (for example) is 8/b sec, so the frequency f of the first (i.e., n=1) harmonic is b/8 Hz.
0
1 sec.
0
b bits
8 bits
T

## Slide 13: Bit Rate vs. Harmonics (cont.)
The number of the highest harmonic passed through is fc/(b/8) or 8fc/b, roughly. That is, the 1st, 2nd, 3rd, ..., and (8fc/b)-th harmonics could pass through without diminution.
N
1
2
:
n
Frequency (Hz)
b/8
2b/8
:
nb/8
nb/8 fc
 n  fc/ (b/8)

## Slide 14: Telephone Line with fc=3000 Hz
Bit Rate
(bps)
T
(msec)
First Harmonic
(Hz)
# Harmonics
sent

## Slide 15: Signal-to-Noise Ratio
S/N
  S: signal power
  N: noise power
dB
  10 log10 S/N
  an S/N ratio of 1000 is 30 dB

## Slide 16: Max. Data Rate of a Channel
Nyquist’s Theorem (noiseless channel)
  H: bandwidth
  V: discrete levels
  Maximum data rate: 2H log2 V bits/sec
Shannon’s Theorem (noise channel)
  H: bandwidth
  S/N: signal to noise ratio
  Maximum number of bits/sec: H log2 (1 + S/N)

## Slide 17: Exercise
Suppose that the bandwidth of a channel is between 3MHz and 4MHz and SN = 24dB.
  (1) what is the capacity of this channel?
  (2) Being able to achieve capacity, how many signaling levels are required?

## Slide 18: Exercise solution
Suppose that the bandwidth of a channel is between 3MHz and 4MHz and SN = 24dB.
  (1) what is the maximum data rate?
    H = 1MHz
    S/N = 251
    C = 106xlog2(1+251)=8Mbps
  (2) Being able to achieve capacity, how many signaling levels are required?
    C=2H log2 V
    V=16