## Slide 1
王昊翔
WANG Haoxiang
hxwang@scut.edu.cn
School of Computer Science & Engineering
国家双语教学试点项目 广东省精品课
COMPUTER NETWORKS 2023 Fall
- Chapter 3. Data Link Layer pter 3. Data Link Layer 2

## Slide 2: Contents of this lecture
Learn 6 elementary DLL protocol
Learn & master sliding-window
Learn & master ARQ（自动重复请求）/PAR
Learn & master piggybacking(捎带确认)
Other: pipeline, NAK

## Slide 3: Elementary DLL protocol
Assumptions:
  The physical layer, data link layer, and network layer are independent processes.
  Machine A wants to send a long stream of data to machine B, using a reliable, connection-oriented service.
  A's data link layer asks for data, the network layer is always able to comply immediately.
  These protocols deal with communication errors, but not the problems caused by computers crashing and rebooting.
  As far as the data link layer is concerned, the packet passed across the interface to it from the network layer is pure data.

## Slide 4: Elementary DLL protocol（cont’d）
3 simplex(单工) protocol：
  An unrestricted simplex protocol
    无限制的单工协议
  A simplex stop-and-wait protocol
    单工的仃—等协议
  A simplex protocol for a noisy channel
    有噪声信道的单工协议

## Slide 5: Protocol Declaration （1/2）
All common data-type、functions are defined as （protocol.h）
Data transmission between NL、PL
PL

## Slide 6: Protocol Declaration （2/2）
Wait_for_event (&event): wait for something to happen
  fram_arrive,
  cksum_err,
  timeout
Timer
  start_timer, stop_timer
  start_ack_timer，stop_ack_timer

## Slide 7: Frame structure
typedef struct{
frame_kind kind;
seq_nr seq;
seq_nr ack;
packet info;
}frame;
Frame header
Frame header
Frame header

## Slide 8: Unrestricted Simplex Protocol (protocol 1)
Protocol 1 (utopia, 乌托邦)
Data are transmitted in one direction only
Both the transmitting and receiving network layers are always ready （随时待命）
Processing time can be ignored （瞬间完成）
Infinite buffer space is available （无限空间）
The communication channel between the data link layer never damages or loses of frames（完美通道）

## Slide 9: Unrestricted Simplex Protocol
Both the sender and the receiver are in an infinite while loop(无限的while循环)
The sender:
The receiver

## Slide 10: Simplex Stop-and-Wait Protocol
Protocol2 ：Drop the unrealistic restriction
  Process abilities in receiver is limited: the receiver has only a finite buffer capacity and a finite processing speed.
How to prevent the sender from flooding the receiver with data?
  simply insert a delay into protocol 1
  the receiver provide feedback to the sender
Protocols in which the sender sends one frame and then waits for an acknowledgement before proceeding are called stop-and-wait
a dummy frame

## Slide 11: Pay attentions
Data traffic is simplex（单工）, but frames do travel in both directions.
The communication channel between the two data link layers needs to be capable of bidirectional information transfer.
  A half- duplex（半双工） physical channel is enough
Data flow
  first the sender sends a frame, then the receiver sends a frame, then the sender sends another frame, then the receiver sends another one, and so on.

## Slide 12: Simplex Protocol for a Noisy Channel
Let us consider the normal situation: a communication channel may make errors.
A scheme using timer and acknowledgement:
  The sender starts a timer after sending a frame.
  The receiver sends back an acknowledgement only when the incoming frame were correctly received.
  The sender will retransmit the frame if the timer expired before
Positive Acknowledgement with Retrasmission
Automatic Repeat reQuest

## Slide 13: PAR(主动确认重传)
What is the fatal flaw in the above scheme ?
  Loss of an acknowledgement
  duplicated frame
How to distinguish a frame being seen for the first time from a retransmission ?
  Use a sequence number in the header of each frame.

## Slide 14: Sliding window protocol
How to improve efficiency of transmission?
  full-duplex （全双工）
  piggybacking （捎带确认）
  sliding window （滑动窗口）（flow control）
Sliding window protocol
  Protocol 4：n=1——basic idea of sliding window
  Protocol 5： Go Back n （回退n帧）
  Protocol 6： Select Repeat （选择性重传）

## Slide 15: Sliding window protocol
How to achieve full-duplex data transmission ?
  Two separate simplex data channels
  One circuit for data in both directions
Piggybacking(捎带确认)
  temporarily delay outgoing acknowledgements so that they can get a free ride on the next outgoing data frame
How long should the receiver wait for piggybacking?
  An ad hoc scheme: waiting a fixed number of milliseconds. （ACK-TIMER）

## Slide 16: Sliding window protocol
A sequence number is associated with each transmitted frame. Sequence numbers range from 0 up to some maximum (2n - 1) circularly.
A window is a list of sequence numbers.
The sender maintains a sending window with sequence numbers corresponding to frames that have been sent but are as yet not acknowledged, or can be sent.
  Whenever a new packet arrives from the network layer, it is given the next highest sequence number, and the upper edge is advanced by one.
  When an acknowledgement comes in, the lower edge is advanced by one.
The receiver maintains a receiving window with sequence numbers corresponding to frames it is permitted to accept.
  When a frame whose sequence number is equal to the lower edge of the window is received, it is passed to the network layer, an acknowledgement is generated, and the window is rotated by one.

## Slide 17: A sliding window of size 1, with a 3-bit sequence number
初始时 发送了第一帧 接收了第一帧 收到第一个确认帧

## Slide 18: Explain
Receiver: after receive frame，check if the sequence number is frame_expected(预期帧号) or not，if it is，receive it and frame_expected+1，that’s sliding receiving-window（接收窗口）。
Sender：When receive acknowledge frame，check if ack_number is next_frame_to_send or not，if it is, get packet from network_layer, and next_frame_to_send+1，that’s sliding sending_window

## Slide 19: Principle of protocol 4
1-bit sliding window protocol （w=1）
Window setting
  Sliding window maximum：MAX_SEQ = 1
  Initial value：seq =0, ack=1（期待接收seq=0）
Window sliding scheme
  A send frame firstly（seq=0, ack=1, A0）
  B receive A0，send back piggyback-acknowledge （seq=0, ack=0, B0）
  A receive acknowledge （to A0），sliding window，send next frame（seq=1, ack=0, A1）
characteristic
  序列号seq和确认值ack“0”“1”交替
  滑动窗口长度W=1，收到确认才移动窗口
  保证按顺序将接收到的正确帧只一次上交网络层

## Slide 20: Normal case of protocol 4
（seq，ack，data）
A
B
(0, 1, A0)
(0, 1, A0)*
(0, 0, B0)
(0, 0, B0)*
(1, 0, A1)
(1, 0, A1)*
(1, 1, B1)
(1, 1, B1)*
(0, 1, A2)
(0, 1, A2)*
(0, 0, B2)
(0, 0, B2)*
(1, 0, A3)
(1, 0, A3)*
(1, 1, B3)

## Slide 21: Abnormal case 1：duplicated
A
B
期望
seq
B
=
0
(0, 1, A0)
期望
seq
A
=
0
(0, 1, A0)
*
交网络层
(0, 0, B0)
期望
seq
A
=1
期望
acq
A
=0
seq
O
acq
O
(0, 0, B0)
期望
seq
A
=1
seq
P
acq
P
(0, 0, B0)*
期望
seq
B
=
1
(1, 0, A1)
(0, 1, A0)
seq
O
acq
O
(0, 0, B0)
期望
seq
A
=1
seq
O
acq
O
(0, 0,B0)
期望
seq
B
=
1
(1, 0, A1)
(1, 0, A1)*
seq
P
acq
P
(1, 1, B
1
)
期望
seq
A
=
0
超时重传
(0, 1, A0)
超时重传
(0, 1, A0)
(0, 1, A0)

## Slide 22: Abnormal case 1：error control
A
B
期望
(0,0)
期望
(0,0)
(0, 1, A0)*
seq
P
ack
O
(0, 0, B0)
期望
(1,0)
seq
P
ack
O
(0, 1, B0)*
期望
(1,0)
(0, 0, A0)
丢弃
(0,
0
, B0)
期望
(1,1)
(1, 0, A1)
(
0,
0
, A0)
丢弃
(1, 0, B1)
期望
(1,1)
(1, 0, A1)
*
seq
P
ack
O
(1,
1, B1)
期望
(0,1)
seq
P
ack
O
(1, 0, B1)
*
期望
(0,1)
(1, 1, A1)
丢弃
(1,
1
, B1)
期望
(0,0)
(0, 1, A2)
(1,
1
, A1)
丢弃
(0, 1, B2)
期望
(
0,0)
(0, 1, A2)
seq
P
ack
O
(
0
,
0
, B
2
)
期望
(
1,0)
(0, 1, A0)
(0, 1, B0)

## Slide 23: Line utilization rate of protocol4（信道利用率）

## Slide 24: Line utilization rate of protocol 4（信道利用率）
An assumption in protocol 4: the time is negligible.
  The transmission time forward or back
  The processing time for the receiver to handle the incoming frame
In fact, the round-trip time can be very large in low rate channel, and the sender is blocked during the period.
Line utilization rate:
  channel capacity is b bps
  frame size k bits
  round-trip propagation time R sec

## Slide 25: Example
Assumption：
  channel capacity b = 50 kbps
  round-trip propagation R = 500 ms
  frame size k = 1000 bit
  Receiver immediately send back acknowledge frame when it receives a frame
Question: how much is line utilization rate?

## Slide 26: Reference key
Time for sending frame
Tf =k/b = 20 ms
Round Trip Time
R = 500 ms
Time from very-beginning to acknowledgement-back
(Tf +R) = 20 + 500 = 520 ms
Line utilization rate
Tf /(Tf +R) = 20/520 = 3.85 %

## Slide 27: Less than 4%
发送方
接收方
Tf
R
Tf + R
W = 1
在发送缓冲区只存储1个待确认帧。

## Slide 28: How to improve line utilization？
Increase maximum sliding-window size W:
  Line utilization = W*Tf / (Tf +R)
  = W* k / (k + bR)
Utopian case: line utilization rate is up to 100%，then maximum sliding-window size is:
W = (Tf +R) / Tf = 520 / 20 =26

## Slide 29: Line utilization rate is 100%
Tf + R
Tf
发送方
接收方
W = 26
连续发送、并在发送缓冲区存储26个待确认帧。
管道化（pipeling）

## Slide 30: Pipeline
Allowing the sender to transmit up to w frames before blocking.
Whenever the product of bandwidth and round-trip-delay is large, a large window on the sending side is needed.
What to do if a frame in the middle of a long stream is damaged or lost?
  Go back n
  Selective repeat

## Slide 31: Protocol 5：go back n
receiver：
  Just discard wrong frame and latter frames(后续帧) （receiving-window is 1）
Sender：
  Resend wrong frame and latter frames

## Slide 32: Basic idea of protocol 5
The receiver's window size is 1, that is to say, the receiver only accepts frames in order.
The receiver discards all frames following an error, sending no acknowledgements.
After time out, the sender retransmits all unacknowledged frames in order, starting with the damaged or lost one.

## Slide 33
Construct a data frame
s.kind=data
s.info=buffer[frame_nr]
s.seq=frame_nr
s.ack=(frame_expected+Max_seq)%(Max_seq+1)
F
A
C
N(S)
P/F
N(R)
Info.
FCS
F

## Slide 34
While (between(ack_expected ,r.ack, next_frame_to_send ))
{
nbuffered= nbuffered-1 （发送窗口上边界）
stop_timer(ack_expected )
inc(ack_expected ) （发送窗口下边界）
}

## Slide 35
ack
5
6
7
0
1
2
3
ack_expected
4
5
6
7
4
对方已正常收到
已发送对方还未确认
入重发缓冲区
MAX_SEQ
窗口大小

## Slide 36: Protocol 6：selective repeat
Receiver：
just discard wrong frame，and store all latter
correct frames
Sender：
Just resend wrong one

## Slide 37: Basic idea of protocol 6
Protocol 6 accepts frames out of order but passed packets to the network layer in order.
  Receives all frames whose sequence number fall within the receiving window
  Doesn’t pass the frame to the network layer until all the lower-numbered frames have already been delivered to the network layer in the correct order.

## Slide 38: An example： 接收方收到非期望的正确帧－缓存
确认
发送
接收方期望接收seq2，缓存其后的正确帧。

## Slide 39: An example： 发送方选择帧seq2重传
确认
发送

## Slide 40: An example： 接收方收到重传帧seq2－排序上交
确认
发送
将帧seq2和接收方缓冲区中的帧正确排序，提交网络层，回送ack=8，滑动接收窗口。

## Slide 41: Function of NAK
Negative acknowledgement (否定确认)
More efficient than protocol 5
  Send back NAK for wrong frame to sender，force sender resend the frame immediately instead of timeout

## Slide 42: Comparison of error control policy and decision of sliding-window size

## Slide 43: Comparison of protocol 5&6
Go back n (protocol 5)
  Sender needs large buffer
  Repeat rate is large (waste bandwidth)，suit for low-error rate environment
Selective repeat (protocol 6)
  Receiver needs large buffer
  Repeat rate is small，suit for bad-quality channel

## Slide 44: Decision of sliding-window size
Protocol 5（回退n帧）
  MAX_SEQ = 7（ Seq=0～ MAX_SEQ ）
  W = 7
  W = MAX_SEQ (sending-window)
Protocol 6（选择重传）
  MAX_SEQ =7（ Seq=0～ MAX_SEQ ）
  W = 4
  W= (MAX_SEQ + 1) / 2 (receiving-window)

## Slide 45: Protocol 5：W = 8，abnormal

## Slide 46: Protocol 5：W = 7，abnormal
Seq = 0
0
Seq = 1
1
Seq = 2
2
Seq = 3
3
Ack = 7
Seq = 4
4
0
Ack = 0
Seq = 5
5
1
Ack = 1
Seq = 6
6
2
Ack = 2
Seq = 7
7
3
Ack = 3
Seq = 0
8
4
Ack = 4
Seq = 1
9
5
Ack = 5
Seq = 2
10
6
Ack = 6
Seq = 3
11
Seq = 4
12
Seq = 5
13
14

## Slide 47: Protocol 6：W=7

## Slide 48: Protocol 6

## Slide 49: Protocol 6

## Slide 50: Protocol 6
第7帧正确提交，重传帧0被认为是正确帧提交，出现重复提交错误。
收到第6帧的确认，认为0～6被正确接收，发送第7～13帧。

## Slide 51: No overlapping
MAX_SEQ=7
W = 7
W = 4

## Slide 52: Protocol 6：W=(MAX_SEQ+1)/2
发送帧0~3等待确认。

## Slide 53: W-Size difference of 3 protocol
One-Bit sliding window (protocol 4):
  0 <= size of Sending window<=1
  size of receiving window=1
Go-back-N (protocol 5)：
  0 <=size of Sending window<=MAX_SEQ
  size of receiving window=1
Selective Repeat (protocol 6)：
  0 <= size of Sending window<= (MAX_SEQ+1)/2
  size of receiving window= (MAX_SEQ+1)/2

## Slide 54: Summary of this lecture
Learn 6 elementary DLL protocol
Learn & master sliding-window
Learn & master ARQ（自动重复请求）/PAR
Learn & master piggybacking(捎带确认)
Learn pipeline
Go back n & selective repeat