## Slide 1
演示文稿是一种实用的工具，可以是演示，演讲，报告等
Networking
俞燕 202192455057
郑爽 202192455055
李睿琦 202192455056
张瑞恒 202192455054
SAIB MD 202169990073
RIP configuration & OSPF configuration

## Slide 2
RIP
1
OSPF
2
RIP vs. OSPF
3
REFERENCES
4
C O N T E N T S

## Slide 3
01
RIP

## Slide 4
Network topology
Experiment devices(for the example): 2 PCs, 2 Router1941s, 3 Copper Cross-Overs

## Slide 5
PC Setup
IP address, subnet mask, default gateway

## Slide 6
Router Basic Setup
Test PC2, R2 for connectivity
Set up R2 interface(R1 is similar to R2)
Firstly, input “en”

## Slide 7
Router Basic Setup
After setting up R1 and R2
PC1 and R1 is still unreachable for PC2 and R2

## Slide 8
Router Basic Setup
Set up router interface and open
R1
interface gigabitEthernet 0/1 ip address 192.168.3.1 255.255.255.0
no shutdown
exit
R2
interface gigabitEthernet 0/1 ip address 192.168.3.2 255.255.255.0
no shutdown
exit

## Slide 9
Router Basic Setup
Set up RIP
R1
router rip
network 192.168.1.0
network 192.168.3.0
version 2
no auto-summary
R2
router rip
network 192.168.3.0
network 192.168.2.0
version 2
no auto-summary

## Slide 10
Test

## Slide 11
Routing Table

## Slide 12
Routing Table
R1 and R2 use the RIP protocol for route learning.
In the routing table, C represents a directly connected route, indicating that the network is directly connected to the interface on the router. R represents a RIP route, indicating a route learned through the RIP protocol.

## Slide 13
R1:Routing Table
The learned routes include the following:
a. Destination network 192.168.1.0/24, learned through a direct connection to the GigabitEthernet0/0 interface (C).
b. Destination network 192.168.2.0/24, learned through the next hop 192.168.3.2 (R), hop count is 120, last update time is 00:00:20, and the interface is GigabitEthernet0/1.
c. Destination network 192.168.3.0/24, learned through a direct connection to the GigabitEthernet0/1 interface (C).

## Slide 14
R2:Routing Table
The learned routes include the following:
a. Destination network 192.168.2.0/24, learned through a direct connection to the GigabitEthernet0/0 interface (C).
b. Destination network 192.168.1.0/24, learned through the next hop 192.168.3.1 (R), hop count is 120, last update time is 00:00:03, and the interface is GigabitEthernet0/1.
c. Destination network 192.168.3.0/24, learned through a direct connection to the GigabitEthernet0/1 interface (C).

## Slide 15
02
OSPF

## Slide 16
Network topology
Experiment devices : 4 PCs, 2 Router, 2 Switches

## Slide 17
Network topology
Place the PC, Switchh and Router

## Slide 18
PC Setup
PC1 and PC2 are connected through the switch.
The ip of PC1 and PC2 are configured as 192.168.1.1 and 192.168.1.2 respectively, and the default gateway is 192.168.1.254

## Slide 19
PC test
PC1 ping PC2

## Slide 20
Router Basic Setup
Connect switch to router 1 and router 2:
configure the Ip of Gig0/0 of R1 and open Git0/0
configure the Ip of Gig0/1 of R1 and open Git0/1

## Slide 21
Topology is ready
Present State
The same can be obtained

## Slide 22
Test
PC3 ping PC1 fail...
What’s wrong?

## Slide 23
OSPF
R1
enable
config t
router ospf 100
network 192.168.1.0 0.0.0.255 area 1
network 192.168.3.0 0.0.0.255 area 1
exit

## Slide 24
OSPF
R2
enable
config t
router ospf 100
network 192.168.2.0 0.0.0.255 area 1
network 192.168.3.0 0.0.0.255 area 1
exit

## Slide 25
Test
PC1 ping PC3
success !

## Slide 26
Routing Table
O: OSPF route
192.168.2.0/24: Destination network and subnet mask
via 192.168.3.2: Next-hop IP address
00:06:54: Time since the last update
GigabitEthernet0/1: Local router interface to use for this route

## Slide 27
03
RIP vs. OSPF

## Slide 28
RIP
RIP, or Routing Information Protocol, is one of the oldest routing protocols. It's a distance-vector protocol that uses the number of hops a packet must pass through as its primary metric for selecting the best path.

## Slide 29
OSPF
OSPF, or Open Shortest Path First, is a more sophisticated protocol. It's a link-state protocol that calculates the most efficient route for data packets based on the cost of the path, which is typically influenced by bandwidth.

## Slide 30
There are differences
RIP vs. OSPF
Feature | RIP | OSPF
Type | Distance-vector | Link-state
Metric | Hop count (max 15) | Cost (bandwidth)
Convergence | Slow | Fast
Updates | Periodic full-table | Incremental LSAs
Algorithm | Bellman-Ford | Dijkstra
Scalability | Small networks | Large networks
Design | Flat | Hierarchical with areas
Configuration | Simple | More complex

## Slide 31
There are deficiencies
RIP vs. OSPF
RIP
OSPF
Operation
periodic updates, based on Bellman-Ford algorithm
event-driven updates, based on Dijkstra's algorithm

## Slide 32
Bellman-Ford Algorithm
RIP Implementation of
Algorithm in Action:
Bellman-Ford Algorithm
Each router calculates the distance to all reachable networks.
The distance metric is the number of hops.
Routes with over 15 hops are considered unreachable, preventing routing loops.
A distance-vector routing algorithm used by RIP to determine the best path to a network.
Calculates the shortest path based on the number of hops between nodes.
RIP's Usage:
Every RIP-enabled router uses Bellman-Ford to update its routing table.
Routers broadcast their routing table to neighbors every 30 seconds.

## Slide 33
Dijkstra's Algorithm
OSPF Implementation of
Algorithm in Action:
Dijkstra's Algorithm
Begins at the router, adding the nearest node to the shortest path tree.
Continues adding the closest non-visited node until all nodes are included.
The cost metric considers factors like bandwidth to determine the shortest path.
A link-state algorithm that calculates the shortest path tree for each route.
Utilizes network topology knowledge stored in the link-state database.
OSPF's Usage:
OSPF routers construct a topological map of the network.
The map is then used to run Dijkstra's algorithm and find the shortest path to all networks.

## Slide 34
There are deficiencies
RIP vs. OSPF
RIP
OSPF
Convergence
&
Efficiency
Slow convergence, can cause temporary loops.
Periodic full-table updates, less bandwidth efficient
Fast convergence, more stable network.
Incremental updates, more bandwidth efficient

## Slide 35
P
Simplicity and ease of configuration.
Low resource usage.
Wide support across devices
RIP
Pros
Cons
-
Slow convergence and potential for routing loops.
Hop count limitation restricts network size.
Full routing table updates are bandwidth-intensive.

## Slide 36
P
Quick adaptation to network
changes.
Scalable to large networks.
Efficient IP address usage
with VLSM/CIDR.
OSPF
Pros
Cons
-
Complexity in configuration and management
Higher resource requirements
Need for careful area design and ABR configuration

## Slide 37
Question for Audiences

## Slide 38
If RIP and OSPF were in a race to update their routes, what would be the likely outcome? (Wrong Answer Only)
A) RIP would take a leisurely stroll and stop for a coffee, allowing OSPF to win with its faster pace.
B) OSPF would get lost counting hops and let RIP hop to the finish line first.
C) They'd both get disqualified for arguing over who has the better algorithm.
D) RIP would insist on using a map from the '90s, while OSPF zooms ahead with GPS navigation.
Question

## Slide 39
04
References

## Slide 40
References
[1] https://blog.csdn.net/m0_72471315/article/details/131060888
[2] https://www.cisco.com/c/en/us/support/docs/ip/open-shortest-path-first-ospf/7039-1.html
[3] https://community.fs.com/article/rip-vs-ospf-what-is-the-difference.html
[4] https://blog.csdn.net/qq_42437085/article/details/106733432

## Slide 41
演示文稿是一种实用的工具，可以是演示，演讲，报告等
Group 14
2023.11
Thanks
THANK YOU FOR WATCHING